## Slide 1: Neural Network Based Digital Twin for a Half-bridge LLC Resonant Converter
Master’s Thesis Defense April 29th, 2024
University at Albany, College of Nanoscale, Science, and Engineering
Nicholas Green
Advisor: Professor Agamy
Committee Members: Professor Elgala, Professor Dahlin

## Slide 2: Outline
Introduction
Previous Works
Converter Model
Data collection and Simulations
Neural Networks
Digital Twin Design
Results/Discussion
Conclusion and Future Work

## Slide 3: Introduction
Ideal Digital Twins can fully emulate a real system only using the same inputs

## Slide 4: Introduction
Unknown internal parameters requires some measurements
Digital Twin characterizes and them emulates

## Slide 5: Previous Work
Averaged
Models
Stochastic
Meta Heuristics
Machine Learning
Known Parameters
Output Prediction
Unknown or Partially Unknown parameters
Unknown parameters
Online Data
Particle Swarm Optimization
Offline Data collection
Outputs/Control predictions
Data Driven
Model Based

## Slide 6: Previous Work
Inputs: Control Gains
Outputs: Reference Error
Inputs: Duty Cycle, Input Voltage, Load Current, past predictions
Outputs: Inductor Current, Output Voltage
Inputs: Input Voltage, Output Current, Past predictions
Outputs: Input Current, Output Voltage
X. Cheng, J. Chen, Y. Chen, X. Zhao, Z. Zhou, Q. Yang, and N. Y. Dai, “Digital-Twin- Driven PI Parameter Evaluation Method for Grid-Connected Converters,” in 2023 4th International Conference on Power Engineering (ICPE), (Macau, Macao), pp. 26–31, IEEE, Dec. 2023.
A. Wunderlich and E. Santi, “Digital Twin Models of Power Electronic Converters Using Dynamic Neural Networks,” in 2021 IEEE Applied Power Electronics Conference and Exposition (APEC), (Phoenix, AZ, USA), pp. 2369–2376, IEEE, June 2021.
G. Rojas-Duenas, J.-R. Riba, K. Kahalerras, M. Moreno-Eguilaz, A. Kadechkar, and A. Gomez-Pau, “Black-Box Modelling of a DC-DC Buck Converter Based on a Recur- rent Neural Network,” in 2020 IEEE International Conference on Industrial Technology (ICIT), (Buenos Aires, Argentina), pp. 456–461, IEEE, Feb. 2020

## Slide 7: Previous Work
Inputs: Input Voltage, Duty Cycle, Frequency, Load Resistance, Inductor, Cap actor, Time (ms), Initial Output Capacitor Voltage
Outputs: Output Voltage, Inductor Current
Inputs: Reference, output, inputs
Outputs: PI gains
H. S. Krishnamoorthy and T. Narayanan Aayer, “Machine Learning based Modeling of Power Electronic Converters,” in 2019 IEEE Energy Conversion Congress and Exposi- tion (ECCE), (Baltimore, MD, USA), pp. 666–672, IEEE, Sept. 2019.
X. Song, T. Jiang, S. Schlegel, and D. Westermann, “Parameter tuning for dynamic dig- ital twins in inverter-dominated distribution grid,” IET Renewable Power Generation, vol. 14, pp. 811–821, Apr. 2020

## Slide 8: Thesis Goals
Converter Characterization with Machine Learning
Increased Complexity
  More accurate switch model/dynamics

## Slide 9: Solid State Transformers
Solid State Transformers take the place of normal transformers
They offer improvements in weight, and size
Due to the architecture, greater control can be implemented such as:
  Voltage sag control
  Limiting current into faults
  DC output
Xu She and A. Huang, “Solid state transformer in the future smart electrical system,”
in 2013 IEEE Power & Energy Society General Meeting, (Vancouver, BC), pp. 1–5,
IEEE, 2013

## Slide 10: Solid State Transformers
Xu She and A. Huang, “Solid state transformer in the future smart electrical system,”
in 2013 IEEE Power & Energy Society General Meeting, (Vancouver, BC), pp. 1–5,
IEEE, 2013

## Slide 11: Half-Bridge LLC Resonant Converter

## Slide 12: Converter Operation: Top Switch On

## Slide 13: Converter Operation: Bottom Switch On

## Slide 14: Converter Modeling
R. Steigerwald, “A comparison of half-bridge resonant converter topologies,” IEEE
Transactions on Power Electronics, vol. 3, pp. 174–182, Apr. 1988.
Take the perspective of looking into the rectifier
Constant DC output voltage reverses to AC Square wave voltage (taking the fundamental approximation)
AC Current expected from resonant converters. Use fundamental AC approximation
Find equivalent resistance using current and voltage reversed through the rectifier
Finally, account for transformer turns ratio

## Slide 15: Converter Modeling

## Slide 16: Inductive Switching
Example of a switch Hard-Switching at Turn On causing switching losses
Turn-On rising current along with the voltage across the switch leads to power losses that increase with frequency limiting power density

## Slide 17: Zero Voltage Switching
Induce Zero Voltage Soft Switching by switching frequency higher than the resonant tank’s natural frequency such that the tank is more “inductive” and lags current such that before switch turn-on, the resonant current discharges the voltage during deadtime

## Slide 18: Converter Modeling

## Slide 19: Converter Modeling
Define:

## Slide 20: Converter Modeling
Name | Value
Converter Gain | 1
LLC Gain | 1
Turn’s Ratio (N) | 
Switch Model | Qorovo SiC Cascode JFET 1200V, 114A DC
Power | 39kW
Input Voltage | 800V
Max Current | 110A RMS / 156A Peak
Name | Value
Converter Gain | 1
LLC Gain | 1
Turn’s Ratio (N) | 
Switch Model | 
Power | 39kW
Input Voltage | 800V
Max Current | 110A RMS / 156A Peak
Define:

## Slide 21: Converter Modeling
Name | Value
Converter Gain | 1
LLC Gain | 1
Turn’s Ratio (N) | 
Switch Model | Qorovo SiC Cascode JFET 1200V, 114A DC
Power | 39kW
Input Voltage | 800V
Max Current | 110A RMS / 156A Peak
Name | Value
Converter Gain | 1
LLC Gain | 1
Turn’s Ratio (N) | 
Switch Model | 
Power | 39kW
Input Voltage | 800V
Max Current | 110A RMS / 156A Peak

## Slide 22: Converter Modeling
Name | Value
Converter Gain | 1
LLC Gain | 1
Turn’s Ratio (N) | 
Switch Model | Qorovo SiC Cascode JFET 1200V, 114A DC
Power | 39kW
Input Voltage | 800V
Max Current | 110A RMS / 156A Peak
Name | Value
Converter Gain | 1
LLC Gain | 1
Turn’s Ratio (N) | 
Switch Model | 
Power | 39kW
Input Voltage | 800V
Max Current | 110A RMS / 156A Peak

## Slide 23: Converter Modeling
Name | Value
Converter Gain | 1
LLC Gain | 1
Turn’s Ratio (N) | 
Switch Model | Qorovo SiC Cascode JFET 1200V, 114A DC
Power | 39kW
Input Voltage | 800V
Max Current | 110A RMS / 156A Peak
Name | Value
Converter Gain | 1
LLC Gain | 1
Turn’s Ratio (N) | 
Switch Model | 
Power | 39kW
Input Voltage | 800V
Max Current | 110A RMS / 156A Peak

## Slide 24: Converter Modeling
Name | Value
Converter Gain | 1
LLC Gain | 1
Turn’s Ratio (N) | 
Switch Model | Qorovo SiC Cascode JFET 1200V, 114A DC
Power | 39kW
Input Voltage | 800V
Max Current | 110A RMS / 156A Peak
Q | 2
 | 0.1
 | 0.3163
Name | Value
Converter Gain | 1
LLC Gain | 1
Turn’s Ratio (N) | 
Switch Model | 
Power | 39kW
Input Voltage | 800V
Max Current | 110A RMS / 156A Peak
Q | 2
 | 0.1
 | 0.3163

## Slide 25: Converter Modeling
Name | Value
Converter Gain | 1
LLC Gain | 1
Turn’s Ratio (N) | 
Switch Model | Qorovo SiC Cascode JFET 1200V, 114A DC
Power | 39kW
Input Voltage | 800V
Max Current | 110A RMS / 156A Peak
Q | 2
 | 0.1
 | 0.3163
Switching Frequency | 100kHz
 | 239nF
 | 10.58H
 | 105.8H
Name | Value
Converter Gain | 1
LLC Gain | 1
Turn’s Ratio (N) | 
Switch Model | 
Power | 39kW
Input Voltage | 800V
Max Current | 110A RMS / 156A Peak
Q | 2
 | 0.1
 | 0.3163
Switching Frequency | 100kHz
 | 239nF

## Slide 26: Data Collection: Experiments
vs
vs
vs in both
Manual Sweeps of parameters were done to get an idea of how changes in some parameters effect measurable parameters.
These can help eliminate negligible parameters to sweep to reduce the simulation time
They can help guide the input selection for more accurate predictions

## Slide 27: Data Collection
Parameter | Base | Range
 | 239nF | 
 | 10.58 | 
 | 105.8 | 
 | 800V | 
 | 20 | 
 | 10 | 
Parameter | Base | Range
 | 239nF | 
 | 800V | 
Passives go beyond the 5-20% tolerances range. Data on degradation
needs to vary around it operating point
ESR taken from real model 220nF film capacitor in lab. Small range around this chosen
ESR taken from large DC-Link Capacitors in lab. Small range around this chosen

## Slide 28: Data Collection
Parameter | Min | Max
ower | 1kW | 39kW
 | 10 | 75
 | 10 | 75
Added | 0 | 50
Added | 0pF | 2550pF
Added | 0pF | 105pF
 | 0.5 nH | 20 nH
Parameter | Min | Max
 | 1kW | 39kW
 | 0pF | 2550pF
 | 0pF | 105pF
 | 0.5 nH | 20 nH
Power range ideally is 0 to full power. Lower limit of 1kW chosen as going lower than that break the converter
Inductor ESR’s chosen in range to account for thermal increases in resistance of copper
range based on switch degradation data plus an additional buffer
Added switch capacitance 30% of datasheet value
Case temps using wide range as thermal simulations are fast
Loop inductance in small range, represents parasitic inductance real connections

## Slide 29: Simulation Setup

## Slide 30: Thermal Approximation
Real Thermal Simulations take too long to reach steady state
  (Switch Losses Junction Temperature)
Instead force an approximate junction temperature to get the corresponding switch losses. Junction temperature was chosen to be in the middle. Ignores self heating effects, and ZVS loss.
  (Junction Temperature Switching Loss Final Junction Temperature)

## Slide 31: Simulation Setup
Solving the gain equation for angular frequency and using numerical solvers, you can find the optimal frequency
To ensure ZVS, choose the max frequency out of all real solutions

## Slide 32: Initial Conditions
Simulating 4 cycles, 1 to adjust and 3 to measure
Without initial conditions, steady state took about 3x more cycles to achieve

## Slide 33: Simulations
Repeating over a range of simulations, a random configuration is selected from the parameter ranges
This configuration is simulated with checks on success, duplicated simulation, and timeout triggers
Both thermal simulations are conducted in the same manner with first finding the average switch powers from the main simulation

## Slide 34: Data Collection
Iterating over all successful simulations, data is gathered from the respective files, (if needed) a post-processing step is done last , and data is formatted into a dataset with a dictionary structure
Just over 6000 sample size dataset

## Slide 35: Neural Networks
Basic Fully Connected Neural Network structure with only an input and output layer. Hidden layers with any size, can be added
Perceptron block diagram where the inner product of the input vector (from all previous perceptrons), and the weight vector is done, added to a bias and passed through a non-linear activation function
Weights, and biases are trainable parameters
The activation function and network structure is a hyperparameters

## Slide 36: Training with Gradient Descent
https://en.wikipedia.org/wiki/Gradient_descent
Loss Functions

## Slide 37: Activation Functions
Sigmoid
Slow to learn (zig-zag search)
Vanishing Gradients
Can still do well for classification or shallow networks
Hyperbolic Tangent (Tanh)
Vanishing Gradients, but gradients are larger than Sigmoid
Tanh
Sigmoid
Gradients

## Slide 38: Activation Functions
Rectified Linear Unit (ReLU)
Fast and simple to compute
Recommended to start with
Might take longer to approximate smooth functions
“Dying ReLU Problem”
Leaky ReLU
Fixes “Dying ReLU”

## Slide 39: Testing
Regression
Where:
Classification
Where:
TP = True Positive
FP = False Positive
TN = True Negative
FN = False Negative

## Slide 40: Digital Twin Design: Sensing
Sensing difficulties with resonant tank voltage due to high frequency, EMI, inductors being implicit in the transformer
Sensing difficulties with high speed switch measurements especially slew rates

## Slide 41: Digital Twin Design

## Slide 42: Results

## Slide 43: Results

## Slide 44: Results

## Slide 45: Results
Narrow Dataset to begin with
Scatter plot shows a good fit, even for rare samples away from main peak

## Slide 46: Results
Again, Narrow Dataset to begin with
Scatter plot shows a good fit, even for rare samples away from main peak

## Slide 47: Results
Boundary predictions can have significant errors. Difference of RMSE to MAE somewhat accounts

## Slide 48: Results
Even more significant boundary predictions can have significant errors

## Slide 49: Results

## Slide 50: Results
Extremely biased dataset
  Top ZVS 98% true
  Bottom ZVS 98.5% true

## Slide 51: Discussion: Boundary Errors

## Slide 52: Discussion: Boundary Errors
Expand Ranges to add buffer
Increase Min/Max samples
Modify Loss function

## Slide 53: Discussion: Narrow Data
Narrow Distribution of certain data
Force certain configurations of the converter to broaden dataset
Simulation without controller

## Slide 54: Discussion: Narrow Data

## Slide 55: Discussion: Wide Networks

## Slide 56: Discussion: Wide Networks
Name | Inputs | # layers + 2 | Width | LR | Batch Size | Best Epoch | Loss Funct | Optimzer | Activation Function | RMSE | MAE | R^2

## Slide 57: Conclusion
Given the model converter, a neural network digital twin was demonstrated to estimate unknown parameters with low error (all below 7% MAE, majority of which were below 3%)
Limitations include related to a smaller dataset of 6k samples, some narrowly ranged parameters. Larger datasets and targeted broadening of certain parameters beyond the chosen ranges may help to better verify this method

## Slide 58: Future Work
Different ML Models
Implement Real Time FPGA
DT Model Expansions
Real Converter Verification
Preloading Data
GTX 750ti
  1.389 PFLOPS FP32
per sample inference

## Slide 59: Future Work: Model Expansion
DT Model Expansions

## Slide 60: Future Work: ML Models
Different ML Models
Time Series Models
Physics Informed Models
Inputs within a window of time
Considers the dynamics
Incorporates known, generalizable physics into training
Reduce data, increase generalizability, encourage learning the physics

## Slide 61: Future Work: ML Models
A. Wunderlich and E. Santi, “Digital Twin Models of Power Electronic Converters Using
Dynamic Neural Networks,” in 2021 IEEE Applied Power Electronics Conference and
Exposition (APEC), (Phoenix, AZ, USA), pp. 2369–2376, IEEE, June 2021
G. Rojas-Duenas, J.-R. Riba, K. Kahalerras, M. Moreno-Eguilaz, A. Kadechkar, and
A. Gomez-Pau, “Black-Box Modelling of a DC-DC Buck Converter Based on a Recur-
rent Neural Network,” in 2020 IEEE International Conference on Industrial Technology
(ICIT), (Buenos Aires, Argentina), pp. 456–461, IEEE, Feb. 2020.

## Slide 62: Future Work: ML Models
S. L. Brunton, J. L. Proctor, and J. N. Kutz, “Discovering governing equations from data
by sparse identification of nonlinear dynamical systems,” Proceedings of the National
Academy of Sciences, vol. 113, pp. 3932–3937, Apr. 2016
M. Raissi, P. Perdikaris, and G. Karniadakis, “Physics-informed neural networks: A
deep learning framework for solving forward and inverse problems involving nonlinear
partial differential equations,” Journal of Computational Physics, vol. 378, pp. 686–707,
Feb. 2019.

## Slide 63: Thank you! Any Questions?